## Slide 1: CE 3372 Water Systems Design
Lecture 17: Storm Drain Design Example

## Slide 2: Storm Drain Design Example
Similar to earlier examples, but more extensive in scope.
The example is intended as a workshop
Module 13

## Slide 3: Problem Statement
Working schematic is provided as a Z-fold

## Slide 4: Problem Statement
At node A8 outflow from the shopping mall is accepted into the storm drain system.
The storm drain outfalls into a channel just downstream of a culvert, which accomodates flow from a 2266 acre watershed.
Hydrology and inlet data on TAB1 in spreadsheet
Design the system, determine hydraulic grade line

## Slide 5: General Information

## Slide 6: Estimate Runoff
Prepare system plan and trial layout
Initial runoff calculations – use rational equation
  C values are composite where applicable
Can be in acres, just don’t mix units

## Slide 7: Estimate Inlet Capture
On grade
Sag
Compute spreadwidth after capture

## Slide 8: Size Conduits
Accumulate CA as move downstream
Add conduit time (uses slope)
Compute required diameter
  round up to commercial pipe size
Compute flow depth at upstream end each conduit
Compute velocity each conduit
Compute HGL from outfall and work upstream

## Slide 9: Software
The illustration is performed in Excel. Appropriate for the example.
Complicated systems can be modeled in
  Geopack-Drainage
  WinSTORM (Deprecated)
  SWMM
    Sophisticated tool, useful for system hydraulics where backwater will be a substantial issue
  HEC-RAS
    Like SWMM, but not really good for storm sewers or looped systems