## Slide 1: CE 3372 Water Systems Design
Lecture 17: storm-water CONDUIT DESIGN

## Slide 2: CE 3372 Water Systems Design
Lesson 16: Storm sewers, inlets, and conduits

## Slide 3: Purposes
Conduits convey Flow from one location to another
  Pipes
  Culverts
  Open channels

## Slide 4: Conduit design
Select size, material, and slope
  Storm sewer – usually desire to operate with free surface (as an open channel)
  Sanitary sewer – similar usually want a free surface
  Size (diameter) is dictated by
    Flow required
    Burial depth relative to drop available

## Slide 5: methods
A good preliminary design can be obtained using a combination of the rational equation and manning’s equation
  Done without regard to downstream boundary conditions
  Needs to be checked using a hydraulic model (like SWMM)

## Slide 6: Preliminary design
Determine discharge in each pipe.
Size using manning’s equation (… in us customary)
Assumes full, but pipes will have free surface

## Slide 7: Preliminary design
Layout of system
  Drainage area and Inlets
  Pipes
  Outfall
  elevations

## Slide 8: Preliminary design
Drainage areas and inlets
  Determine inlet time of concentration
  Determine drainage area runoff coefficient

## Slide 9: Preliminary design
Pipes (Start upstream)
  Select pipe size
    Design guidelines
    Discharge criteria
    Velocity criteria
  Determine pipe travel time
From criterion
Adjust
Notes: 𝑉=1.49/𝑛 〖(𝐷/4)〗^(2/3) √𝑆

## Slide 10: Preliminary design
  At most upstream inlet
    Compute QP=CiA to the inlet from inlet time
    Size pipe from this inlet to hold QP
    ADD pipe travel time to inlet time
    Move to next node
Notes: 𝑉=1.49/𝑛 〖(𝐷/4)〗^(2/3) √𝑆

## Slide 11: Preliminary design
  At NEXT upstream inlet
    Compute QP=CiA to the inlet from inlet time
    Size pipe from this inlet to hold QP
    ADD pipe travel time to inlet time
    Move to next node
Notes: 𝑉=1.49/𝑛 〖(𝐷/4)〗^(2/3) √𝑆

## Slide 12: Preliminary design
  AT JUNCTION AND INLET
    Choose largest of:
    Local inlet time
    Upstream node+travel time
  Compute Qp LEAVING THE JUNCTION FROM:
  SIZE next pipe from this qp
local
Notes: 𝑉=1.49/𝑛 〖(𝐷/4)〗^(2/3) √𝑆

## Slide 13: Preliminary design
  Continue downstream in same fashion (from upstream to junction) until reach outlet
  Accumulate CA values and Tc as move downstream
  Checks include that all areas add up to total area
  Tc should be increasing in value as move downstream
local
Notes: 𝑉=1.49/𝑛 〖(𝐷/4)〗^(2/3) √𝑆

## Slide 14: Preliminary design
At outlet should have:
  Pipe sizes
  Pipe discharges
Next check hydraulics
  SWMM – enter QINLET directly and check pipe hydraulics
  SWMM – Approximate rational in SWMM to check a design hyetograph
  Use SWMM results to adjust design and produce a HGL drawing
local
Notes: 𝑉=1.49/𝑛 〖(𝐷/4)〗^(2/3) √𝑆

## Slide 15: Next Time
Storage Node (Details)
  Used to mimic detention ponds
  Used to mimic lift-station wet-well sumps