## Slide 1: CE 3372 water systems design
Design Guidelines – drinking water supply Part 2 (fall 2020)

## Slide 2: Project layout
Notice that most of the manuals spend considerable space explaining how drawings are to be submitted for approval.
The actual layout is flexible (within right-of-way) and up to the hydraulic engineer to some extent.
A designer would typically use some version of the following to design a new water distribution system:

## Slide 3: Project layout - Continued
A designer would typically use some version of the following to design a new water distribution system:
  Set up the system grid on the area plan. Aerial photo plots to scale are excellent tools
  Allocate average daily demands at nodes;
  Determine the peak factors;
  Estimate fire demands;
  Project demands for future expansion of the service areas.

## Slide 4: Project layout - Continued
A node is considered a junction point in a system where a demand can be attributed/assigned.
Models use the nodes to calculate the system demands, pressures, water quality, and velocity.
These items are usually prescribed in guidance documents with minimum/maximum acceptable values.

## Slide 5: Project layout - Continued
The practical design of a water system without the use of water distribution modeling software is possible, but requires a logical, economical approach of laying out the system (and some roll your own calculations)
  professional quality software is inexpensive (free) so there is really no reason to design a system without using a hydraulic model - hence the guidance documents nearly demand a model.

## Slide 6: Project layout - Continued
Commercial software is usually far easier for a designer to use and integrated into other design tools, but is computationally about the same as free software
  by all means a designer should use commercial software when it is available.

## Slide 7: Existing data
The designer will need reliable sources to determine demands.
  Obviously a discussion with the owners is critical but the actual quantities will have to be calculated for a design situation.
A land use plan or zoning map will help to determine the future demands.
Notes: A land use plan or zoning map will help to determine the future
demands. Use standards developed by the American Water Works Association for
typical demands for a particular land use, such as industry, residential density, etc.

## Slide 8: Existing data
The demands need to be compiled and situated on an area map.
Once complete this map can help determine node locations and pipe diameter for the system schematic
Notes: A land use plan or zoning map will help to determine the future
demands. Use standards developed by the American Water Works Association for
typical demands for a particular land use, such as industry, residential density, etc.
When an existing system is modeled the process is known as analysis. Modeling
during the course of designing a project is much more dicult. While modeling an
existing system requires input of available of existing data. The level of accuracy
and detail of data depends on the available data and map accuracy. When a system
is being designed and modeled there is a trial and error process involved. Topo-
graphic maps, general routes, and pipe sizes are assumed. The process of developing
a schematic for modeling is very dynamic. A schematic of a proposed system for an
existing community may be changed several times based on public input, political
divisions, and cost comparisons. Much like an electrical schematic or roadway system
layout, a pipe network will have nodes (junctions). Small systems can be greatly
aected by small changes in demand and design. Large metropolitan systems are less
aected by local demand changes at nodes.

## Slide 9: Pipe diameter
The selected pipe diameters affect system hydraulics.
The trench is the biggest cost, and the hydraulics should be used to set adequate pipe sizes.
  Designers need to determine the proper pipe size in order to meet peak demands and fire protection while maintaining an adequate dynamic pressure in the system.
Notes: The selected pipe diameters can aect the model signicantly. There are economic
considerations in choosing the pipe diameters, many jurisdictions specify minimum
pipe sizes -- sometimes these are still too small and the designer needs to acknowl-
edge this fact. The trench is the biggest cost, and the hydraulics should be used to
set adequate pipe sizes. Designers need to determine the proper pipe size in order
to meet peak demands and re protection while maintaining an adequate dynamic
pressure in the system. During design, once a model is built using good reasoning or
assumptions, model runs will give results and demonstrate pipes that are too small
either by hydraulic grade line or by low pressure. If you review the model output and
see a signicant drop in pressure, increase the pipe diameter and try another run.
Finding which pipe to increase may not be an easy task.

## Slide 10: Pressure zones
Pressure zones are set up to regulate pressure in locations where large grade changes will create too much pressure at the lower end of the system and not enough pressure in the higher ends.
  More than an 80 feet differential will require a pressure zone.
  In areas of even larger grade differentials, such as hill country or mountain communities, several consecutive pressure zones may be needed.
Notes: Pressure zones are set up to regulate pressure in locations where large grade changes
will create too much pressure at the lower end of the system and not enough pressure
in the higher ends. A dierential of less than 60 feet (25.4 psi) does not require a new
pressure zone. More than an 80 feet dierential generally will require a pressure zone.
In areas of even larger grade dierentials, such as hill country or mountain commu-
nities, several consecutive pressure zones may be needed.

## Slide 11: Pressure zones
The following equations can assist in determining the HGLs for the pressure zones.
  HGLMIN = Highest Elevation + (2.31x Minimum Working Pressure)
  HGLMAX = Lowest Elevation + (2.31x Maximum Working Pressure)
Notes: The following equations
can assist you in determining the HGLs for the pressure zones. HGLMIN = Highest
Elevation + (2.31x Minimum Working Pressure) HGLMAX = Lowest Elevation +
(2.31x Maximum Working Pressure)
It is important to converting pressures to the HGL because most models are based
on the HGL. In the case of multiple pressure zones, it is important to use the service
connection datum instead of the pipe elevation or valve elevation, in these equations.
Use of accurate topographic maps is very important in setting up pressure zones. As
the designer you must layout the zones in order to determine the corridors so that
survey eld crews can be sent out to collect accurate data for the design phase.

## Slide 12: Junction Location and Elevation
Location of junctions will depend more upon the planned layout of the project site than the affect they will have upon the hydraulic model.
  In general grid distribution node locations have little affect upon the overall model since there are customer demands along the real system between nodes. Node locations and their elevations are more relative in large transmission mains.
  Nodes generally should be placed at the lowest elevation of a looped system where the grades uctuate signicantly.
Notes: Location of junctions will depend more upon the planned layout of the project site
than the aect they will have upon the model. In general grid distribution node loca-
tions have little aect upon the overall model since there are customer demands along
the system between nodes. Node locations and their elevations are more relative in
large transmission mains. Nodes generally should be placed at the lowest elevation
of a looped system where the grades uctuate signicantly. This is not always pos-
sible. When junctions are put at lower elevations, the distribution and capacity are
improved. In systems where pressures are expected to uctuate or are generally low,
it would be good practice to relate system node elevations to the highest point of
service. Other choices of datum could be relative to the ground, or to the center of
the pipe. Be consistent in order to accurately represent the model once a relative
datum is chosen.

## Slide 13: Materials
The pipe materials will effect system performance.
Water distribution systems are built from ductile iron pipe, ABS, PVC, and HDPE.
  All are good materials for specific applications and various fittings to join different materials are available.
Different jurisdictions may specify specific materials; the designer needs to read the guidance document for the specific locale.
Notes: Location of junctions will depend more upon the planned layout of the project site
than the aect they will have upon the model. In general grid distribution node loca-
tions have little aect upon the overall model since there are customer demands along
the system between nodes. Node locations and their elevations are more relative in
large transmission mains. Nodes generally should be placed at the lowest elevation
of a looped system where the grades uctuate signicantly. This is not always pos-
sible. When junctions are put at lower elevations, the distribution and capacity are
improved. In systems where pressures are expected to uctuate or are generally low,
it would be good practice to relate system node elevations to the highest point of
service. Other choices of datum could be relative to the ground, or to the center of
the pipe. Be consistent in order to accurately represent the model once a relative
datum is chosen.