## Slide 1: CE 3372 Water Systems Design
Lecture 18: Introduction to SWMM

## Slide 2: SWMM
Storm Water Management Model
  Originally by University of Florida in the 1970’s
  V1-4 are FORTRAN
  V5 re-factored into C++
The computation engine is mature
  MIKE URBAN
  SOBEK
  XP-SWMM
  Civil Storm
Notes:     Interestingly V4 and V5 are still in use; such a fork is uncommon in the software business

## Slide 3: SWMM
Started as a simplified hydraulic model, evolved into an integrated hydrology-hydraulics model
  Pretty useful in urban settings
  Used for BMP performance estimation
  Used for LID performance estimation

## Slide 4: Download and Install
Google “EPA-SWMM” to find the software
Download the self-extracting archive
Download the user manual

## Slide 5: Tour of the Interface
Nodes and Links
Outfall
Sub-catchments and Rain gages
Date/Time
Hydraulics
Hydrology

## Slide 6: Nodes
Junction Nodes
Storage Nodes
  Invert Elevations
  Flooding

## Slide 7: Junction (Node)
Ordinary junction connects hydraulic elements (links)
Junction attributes are:
  Invert elevation (elevation of the bottom of the node)
  Max elevation (elevation of top of node)
    Set to land surface to plot profile grade line in SWMM
    Set to land surface + added depth for dual (surface+subsurface drainage)
When program runs, depth at the node is computed, but there is no storage (node has zero area)

## Slide 8: Junction (Node)
Ordinary junction just connects pipes N-1, N, and N+1

## Slide 9: Junction (Node)
If flooding occurs, it is only considered when HGL is above node Max. Depth
Node not flooded; pipes are surcharged
Node flooded; pipes are surcharged

## Slide 10: Junction (Node)
Flooded node attributes:
  How deep is the flooding allowed (surcharge depth) above the top of the node
  What is the ponded area during surcharge – treats the node as a vertical wall storage tank
Ponded Area
Ponded Depth
Max. Depth
Invert Elevation
Invert Elevation + Max. Depth

## Slide 11: Example 1 : Rectangular Channel
Steady flow over a weir; depth at the weir is 2.0 meters. Determine the water surface profile for a distance 2000 meters upstream using SWMM. Sketch:
  Hydraulic Data:
    Rectangular B = 1 m
    Steady flow Q = 2.5 CMS
    So = 0.001
    n = 0.025
    Dx = 200 meters
    Outfall boundary == fixed

## Slide 12: Example 2 : Flow in a Sewer
Discharge in a 3 mile long, 60-inch RCP sewer is 50 MGD. What is the flow depth if the entire sewer is on a 0.1% slope and the downstream boundary (outfall) is a normal depth condition?
  Hydraulic Data:
    Circular: 60-inches (5 feet)
    Steady flow Q = 50 million gallons per day (MGD)
    So = 0.001
    n = 0.015
    Dx = 2640 feet (use 6 links)
    Outfall boundary == normal

## Slide 13: Next Time
Runoff from a sub-catchment.
Hacking “Rational” method in SWMM